## Slide 1
Regynix
Cadence Genus Retiming Synthesis Flow
Automated Register Retiming for Timing Closure
Lead Engineer: Jairus Samraj Solomon
Cadence Genus 21.14
RTL-to-Gates Flow
VIT Chennai · May 2026

## Slide 2
What This Project Does
OVERVIEW
Automated RTL Synthesis with Register Retiming
01
Read RTL Verilog
Ingests testdesign.v – a multi-output FIR-like datapath with 4 parallel processing streams
02
Apply Timing Constraints
Reads testdesign.sdc defining a 200 MHz clock (5 ns period), I/O delays, and false paths
03
Enable Retiming
Activates Genus register retiming to rebalance pipeline stages and reduce critical-path delay
04
Synthesize & Report
Runs syn_gen → syn_map → syn_opt and emits QoR, timing, area, and gate reports
Main Objective: Improve timing performance through automatic register retiming during RTL synthesis

## Slide 3
Project Inputs
FILE STRUCTURE
Key Input Files & Their Purpose
File | Type | Purpose
testdesign.v | RTL Verilog | Top-level design — 4-input datapath with 16 FIR coefficients
testdesign.sdc | Timing Constraints | 200 MHz clock, I/O delays (2.25 ns), setup uncertainty (1.25 ns)
LIB/*.lib | Standard Cell Library | 5 timing libs: slow.lib, pll.lib, CDK_S128x16, CDK_S256x16, CDK_R512x16
run.tcl | Synthesis Script | Complete end-to-end Genus flow: read → elaborate → retime → syn_gen/map/opt
SDC Key Parameters
Clock Period: 5.00 ns (200 MHz)
Setup Uncertainty: 1.25 ns
Input / Output Delay: 2.25 ns
Design Statistics
Module: testdesign (Verilog-2001)
Outputs: 4 × 10-bit vectors (xout_15_1..4)
Inputs: 4 × 5-bit data + 16 × 8-bit coefficients

## Slide 4
Overall Synthesis Flow
ARCHITECTURE
Eight-Stage RTL-to-Gates Pipeline
Read RTL
read_hdl -v2001
Elaboration
elaborate $design
Design Checks
check_design
Read Constraints
read_sdc *.sdc
Enable Retiming
set_attr retime true
syn_gen
Generic Synthesis
syn_map
Technology Mapping
syn_opt
Incremental Opt
★ Critical Step
Phase 1: Initialization
Phase 2: Pre-Synthesis
Phase 3: Synthesis
Generated Outputs
testdesign_generic.db
testdesign_map.db
testdesign_incr.db
reports/ (QoR, timing, area, gates)
Retiming Effect
WNS Before
−4221 ps
WNS After (syn_opt)
−883 ps
TNS Improvement
−890k → −295k ps

## Slide 5
run.tcl — Library Setup & Design Initialization
STEP 1–2
Configuring the Synthesis Environment
run.tcl — Library & Initialization
# Library setup
set_attribute library {
./LIB/slow.lib
./LIB/pll.lib
./LIB/CDK_S128x16.lib
./LIB/CDK_S256x16.lib
./LIB/CDK_R512x16.lib
} /
# Top-level module
set design testdesign
# Synthesis effort levels
set SYN_EFF medium
set MAP_EFF medium
Standard Cell Libraries
5 libs loaded: timing-accurate slow-corner models plus SRAM/RAM macros (CDK_S128x16, CDK_S256x16, CDK_R512x16)
Top Module Declaration
set design testdesign — tells Genus which RTL module is the synthesis root
Effort Levels
'medium' effort balances runtime vs quality; can be raised to 'high' for timing closure
TNS Optimization
set_attribute tns_opto true — enables Total Negative Slack optimization across all violating paths
Debug flags: retime_debug and retime_debug_path are enabled → Genus writes retiming move logs to st_debug_logs/ for post-run analysis.

## Slide 6
run.tcl — Read RTL, Elaboration & Design Checks
STEP 3–5
Parsing, Building the Hierarchy, and Validating the Design
RTL Read & Elaborate
# Read Verilog RTL
read_hdl -v2001 testdesign.v
# Build internal hierarchy
elaborate $design
# Check design integrity
check_design
check_design -undriven -unloaded \
-multidriven -unresolved \
-constant > check_design.report
# Timing lint
report timing -lint -verbose
read_hdl -v2001
Parses Verilog-2001 syntax
Registers all modules and parameters
Flags syntax errors immediately
elaborate $design
Resolves module hierarchy
Expands parameters and generates nets
Creates the internal netlist object
check_design + timing lint
Detects undriven / unloaded signals
Flags multidriven nets
Reports constraint issues before synthesis
report timing -endpoints -num_paths 10 > CritPath_SDC.rpt ← pre-retiming critical path baseline (WNS = −4221 ps)

## Slide 7
run.tcl — Reading SDC Timing Constraints
STEP 6
Defining Clock, I/O Delays, and False Paths
testdesign.sdc (excerpt)
set CLK_200_PERIOD 5.00
set CLK_200_S_UNCERT 1.25
set CLK_200_INPUT_DELAY 2.25
set CLK_200_OUTPUT_DELAY 2.25
create_clock -period 5.00 [get_ports clk]
set_clock_uncertainty -setup 1.25 clk
# Async reset — excluded from timing
set_false_path -from [get_ports rst_l]
# Synchronous inputs (xin_1..4)
set_input_delay 2.25 [get_ports $clk_inputs] \
-clock [get_clocks clk]
# Outputs (xout_15_1..4)
set_output_delay 2.25 [get_ports $clk_outputs] \
-clock [get_clocks clk]
Constraint | Value | Impact
Clock Period | 5.00 ns | Target frequency: 200 MHz
Setup Uncert. | 1.25 ns | Guard-band reduces usable window to 3.75 ns
Input Delay | 2.25 ns | Time consumed by upstream logic
Output Delay | 2.25 ns | Time reserved for downstream logic
False Path | rst_l + 16 coef ports | Excluded from timing analysis
⚠ Why Constraints Matter
Without SDC, Genus has no timing target and retiming has no objective — the tool cannot determine which register moves improve slack.
read_sdc Constraints/testdesign.sdc ← TCL command loads the above constraints into the Genus timing engine

## Slide 8
run.tcl — Enabling Register Retiming ★ Most Critical Step
STEP 7
Allowing Genus to Move Registers Across Combinational Logic
Retiming Activation Commands
# Enable retiming on all instances
set_attr retime true /des*/*
# Allow reset logic to be retimed
set_attr retime_optimize_reset true /
Move Registers Forward
Pushes flip-flops past combinational gates to reduce logic depth on long paths
Move Registers Backward
Pulls flip-flops through gates to absorb slack from short, fast paths
Balance Pipeline Stages
Equalises delay across parallel paths so no single stage dominates
Reduce Critical Path
WNS improved from −4221 ps → −883 ps (79% reduction in worst violation)
BEFORE
FF
Long
Logic
FF
Short
Logic
−4221 ps
Imbalanced paths
→
RETIME
AFTER
FF
Bal.
Logic
FF
Bal.
Logic
−883 ps
Balanced paths

## Slide 9
run.tcl — Synthesis Stages: syn_gen → syn_map → syn_opt
STEP 8–10
Three Progressive Stages of RTL-to-Gates Synthesis
syn_gen
Generic Synthesis
Converts RTL to technology-independent Boolean logic. Applies initial retiming transformations — register moves determined here.
QoR Snapshot
23,402 leaf instances
72,981 area units
WNS: −2688 ps / TNS: −890k ps
write_db → testdesign_generic.db
syn_map
Technology Mapping
Maps generic gates to actual standard cells (NAND, FF, buffers) using timing-accurate library data. Area drops ~50%.
QoR Snapshot
16,167 leaf instances
36,839 area units
WNS: −2182 ps / TNS: −832k ps
write_db → testdesign_map.db
syn_opt
Incremental Optimisation
Final pass: buffer insertion, cell resizing, additional retiming. Largest improvement in WNS — slack cut by ~60% from map stage.
QoR Snapshot
22,799 leaf instances
44,881 area units
WNS: −883 ps / TNS: −295k ps
write_db → testdesign_incr.db
WNS: −2688 ps
→
WNS: −2182 ps
→
WNS: −883 ps ✓ Best

## Slide 10
Output Reports & Final Results
RESULTS
Understanding the Generated Reports
Report File | Stage | Key Information
gen_qor.rpt | syn_gen | WNS −2688 ps, TNS −890k, 23,402 cells, area 72,981
map_qor.rpt | syn_map | WNS −2182 ps, TNS −832k, 16,167 cells, area 36,839
iopt_qor.rpt | syn_opt | WNS −883 ps, TNS −295k, 22,799 cells, area 44,881
TimingPath_Opt.rpt | syn_opt | Top 10 critical endpoints; worst: csa_tree_add…_reg/D
CritPath_SDC.rpt | Pre-syn | Baseline WNS −4221 ps (before retiming)
map_area.rpt | syn_map | Detailed cell area and physical hierarchy
map_gates.rpt | syn_map | Gate-level statistics (NAND, FF, buffer counts)
Key Timing Metrics
Slack:
Required Time − Arrival Time. Positive = timing met.
WNS:
Worst Negative Slack — the most critical single path violation.
TNS:
Total Negative Slack — sum of all violating path slacks.

## Slide 11
Conclusion
Regynix demonstrates how Cadence Genus performs automated retiming optimization — delivering a 79% improvement in worst-case timing slack through intelligent register redistribution across pipeline logic.
Key Concepts Demonstrated
RTL Synthesis Flow
Read → elaborate → check → constrain → synthesize
Retiming Mechanism
Genus moves FFs forward/backward through logic to balance pipeline
SDC Constraints
Clock (200 MHz), I/O delays, false paths define the timing target
Results Achieved
Technology Mapping
Generic Boolean → actual NAND/FF/buffer standard cells
QoR Analysis
WNS/TNS metrics across three synthesis stages show steady improvement
Result
WNS improved from −4221 ps (baseline) to −883 ps (syn_opt)
Regynix · Cadence Genus Retiming Flow · Jairus Samraj Solomon · VIT Chennai 2026